SMART i-Oximeter

SMART i-Oximeter, the new generation of inteligent and hand-held oximeters, is specially designed to be applicable in Telemedicine Field. It features full functions for SpO2 measurements, wireless information transmission and powerful capacity of memory. Its Infrared Interface allows data transmission to IR portable printer for data print-out and Bluetooth technology provides real-time data transfer to Telemetry Station. Users can also apply to optional i-Smart Link I Software to link with computer through USB port for data analysis. Its ID design with ergonomic shape and user-friendly operation is considered not only a helpful instrument for professional purpose, but also satisfies the needs for home care applications in prospective future. Whenever you need a reliable and accurate SpO2 measurement device for continuous monitoring or spot-checks, rely on i-Oximeter to meet your highest requirements.

# Text boxes

SPECIFICATIONS

Model No.:      MD-620P  i -Oximeter

General Specifications

Display:           Bright and easy-to-read LCD with Backlight , SpO2, Pulse Rate, Memory, Strength of pulse, Battery Status, clock and Symbol function.

Pulse Strength:      Light bar indicator

SpO2 Range:       0% ~ 100%

SpO2 Accuracy:     80% ~ 100 ± 2 %

65% ~ 79 ± 3 %

Pulse Rate Range:   30 B.P.M. to 250 B.P.M.

Pulse Accuracy:     ± 1% of full scale

Sound:			  Tone function & volume by digital

Adjustment

Memory Trend:     48 Hours / 6sec recording rate

Data Transfer:      IR-Printer, Bluetooth, USB port.

Housing:          Stable easily cleanable ABS plastic

Temperature:       0°C~ 55°C (Operating)

-20°C ~55°C (Storage)

Humidity:        15 ~ 95% (Operating)

10 ~ 95% (Storage)

Power Requirement: 4 pcs “AAA” Size battery

Quick measurement: 6~8 seconds depend on pulse rate

Power Management: AC/DC Selectable

4 pcs “AAA” Size battery

Dimensions:       115 x 65 x 43 mm

Weight:           160 g (Including batteries)

Quality System:    ISO 9001, ISO 13485, GMP

Safety:             0434

FEATURES

* Large LCD Display with backlight

* Compact and modern design

* Quick response of SpO2 & Pulse Rate

* Pocket size for long time monitor

* Low power consumption

* Use “ AAA” battery

* Battery life approx. 40 hours continuous use

* Low battery indication (30 minutes remains)

* Memory size 48 hours

* Pulse strength by full scale light bar indicator

* Saturation Dependant Pulse Tone

* Adjustable Volume for Pulse Tone

* Data printing by IR printer (Option)

* Data manager by i -Smart Link I (Option)

* Online Transmission by Bluetooth

ACCESSORY

SpO2 standard sensor:. R004i, AC/DC Adaptor

4 pcs “AAA” batteries, Owner’s manual,

Carry-bag

OPTIONAL

Telemetery Station: MD-210TB

IR Portable oximeter

Disposable sensors: D001-D003

Extendtion cable: E009i

Reusable sensors:R003i,R004i, R005i, R008i

i-Smart Link I

Distribution:

|  | Kalas, s.r.o. Ul. Slov. Partizánov 1131/51 017 01 Považská Bystrica, Slovakia Tel/Fax: +421 (0)42 4326907 E-mail: info@kalas.sk • www.kalas.sk |
| --- | --- |